## Slide 1: Op Amps for Everyone
CH 4 Single Supply Op Amp Design Techniques

## Slide 2: Problems of Using Inverting Configuration with Positive Supply
Positive input will not work since output cannot go negative
Works only marginally with small negative input because op amps are highly susceptible to reverse voltage breakdown

## Slide 3: Circuits to Implement VOUT = +m VIN ± b
Apply VIN to the + terminal
Like-wise, b goes to + or – terminal as needed
+b
-b

## Slide 4: Circuits to Implement VOUT = -m VIN ± b
+b
-b
Apply VIN to the - terminal
Due to VIN going negative, these circuits require special protection

## Slide 5: Circuit Protection for Op Amp Input in Inverter Circuits
Use a schottky diode to keep the red node to above -200mV.
If op amp has no power, and input is negative, the entire negative input will appear at the red node.

## Slide 6: Circuit to implement: VOUT = +m +VIN + b
Equations are derived by using superposition
VREF must be low in noise --- any noise in VREF might be amplified
Resistors can be decreased to reduced input current error (more current = less of that current going into op amp’s +/- terminals)
Smaller resistors leads to better frequency response

## Slide 7: Circuit to implement: VOUT = +m +VIN - b
In writing the contribution from VREF, the high lighted part is treated as a Thevenin source.
Assume RG > R1 || R2 to simplify finding the needed resistor ratios.

## Slide 8: Using VCC as VREF
Using VCC as VREF can save money, but be sure to filter the VCC
This capacitor is for filtering.