## Slide 1: Op Amps for Everyone
CH 8 --- Current-Feedback Op Amp Analysis

## Slide 2: CFA Model
GB and GOUT around 1
ZB usually < 50 ohm
Z = Transimpedance
Measured in (V/A) = Ω

## Slide 3: Non-inverting CFA Circuit Analysis

## Slide 4: Non-inverting CFA Ideal Equation
Requirements:
ZB the input buffer output impedance is zero
Z the transimpedance is very high
CFA departs from the ideal more than the VFA does

## Slide 5: The Inverting CFA Ideal Equation
Note the input resistance seen will be (ZG + ZB || ZF)
CFA is not good for the differential amplifier configuration due to the input impedance mismatch

## Slide 6: Loop Gain Equation

## Slide 7: CFA Stability
Z has two poles just like voltage op amps
ZF, ZB, and ZG reduce Z so that the loop gain cross unity at phase < 180 degrees
ZB is internal and ZG has little effect
ZF is the key component to be adjusted
Datasheet will advise an optimal value for ZF . A higher ZF will increase stability but decrease bandwidth.

## Slide 8: Stability and Input Capacitance
Tina analysis of adding input capacitance in parallel withCG
W(s) = AM1 / VS1
Loop gain will be W(s) * Z
Pole location:
Large enough CG will move pole to lower frequency, adding phase and creating instability

## Slide 9: Stability and Feedback Capacitance
Tina analysis of the feedback circuit with a capacitor in parallel with RF , W(s) = AM1 / VS1
Full loop gain equation is W(s) * Z.
The zero will occur before the pole, so the loop gain AB will cross unity later.
Large enough CF will make AB cross unity later, thus creating instability.
Even small values of CG and CF are bad for stability, so layout is critical.