## Slide 1: Fundamentals of Power Electronics, Second Edition
CH13 - Basic Magnetics Theory
Last modified May 20, 2007

## Slide 2: References
“Fundamentals of Power Electronics”, second edition, by Robert W. Erickson and Dragan Maksimovic, CH 13

## Slide 3: Magnetomotive Force (F)
F = magnetomotive force
H = magnetic field
Simplest case: F = H * l

## Slide 4: Magnetic Flux (Ф)
Ф = Magnetic flux
B = Flux density
dA = vector normal to the surface
Simplest case: Ф=BA

## Slide 5: Faraday’s Law
For uniform flux distribution:
v(t) = A * dB/dt
Lenz’s law – polarity of v(t) will induce a current that will counter the flux change.

## Slide 6: Ampere’s Law
i(t) = total current passing through interior of path
For the case of uniform H(t), F(t) = H(t)ℓm = i(t)

## Slide 7: Permeability (μ)
μ0 = permeability of free space
μr = relative permeablity

## Slide 8: Magnetics Units

## Slide 9: Basic Relationships Summarized

## Slide 10: Inductance

## Slide 11: Core Saturation
When DC level of i(t) is small, di/dt  dH/dt  dB/dt  v(t)
When DC level of i(t) is sufficiently large, di/dt  dH/dt, but dH fail to produce any dB, and dB = 0. Then v(t) will be zero, and the inductor looks like it’s shorted, with L being very small.

## Slide 12: Reluctance
Reluctance:
Reluctance is how easily flux flows given a certain MMF

## Slide 13: Inductor with Air Gap

## Slide 14: Effect of an Air Gap
Rg > Rc , Rg makes L smaller
μ changes according to temperature and operating point, so Rg stabilize inductance value
Larger Rg reduce flux for the same current, so Rg allows inductor to operate at higher DC current.

## Slide 15: Transformer
Ideal transformer assumes infinite μ, so RФ = 0.

## Slide 16: Transformer with non-infinite μ
and
together becomes:

## Slide 17: Magnetizing Inductance
Equivalent
Circuit

## Slide 18: Output Inductor Saturation
Saturation can be determined based on H*ℓ = n*i
The current has a DC component that is related to the loading, and an AC component related to inductance.
Increase in n will increase inductance and reduce AC component, but increase overall “H”
The DC component being the dominant one, so the net effect of increasing n is to increase H to create saturation
Reduce n or reduce Idc to solve saturation

## Slide 19: Transformer Saturation
From the view of H*ℓ = n*i, the n*i is actually n1i1+n2i2, so that the total H is close to zero
The total i is mostly AC that will depend on inductance. Changing n will change i as well, so it’s not clear how increasing n will affect saturation.
The cause of saturation really comes from applying too much volt-second, or that ∫v(t) dt becomes too large.
Use n*BAC = ∫v(t) dt to see that increasing n or Ac will reduce B
Increase n or increase Ac to solve saturation

## Slide 20: Leakage Inductance - Concept
Leakage inductance is due to flux that leaks into the air and links one winding but not the other

## Slide 21: Leakage Inductance - Circuit
L12 is called mutual inductance
L11 and L22 are called self-inductances

## Slide 22: Leakage Inductance – Circuit Solution for L12
When i1(t) = 0:
There’s no voltage across Lℓ1

## Slide 23: Leakage Inductances – Performance Parameters
Effective turns ratio:
Coupling coefficient (0 < k < 1):
When there is no leakage inductance:
  Coupling coefficient = 1
  Effective turns ratio becomes n2/n1

## Slide 24: Core Loss – The Equation
Combines into:
The above is loss per cycle; so total power dissipation gets higher for higher switching frequency.
During one cycle, v(t) is positive some of the time and negative rest of the time.

## Slide 25: Eddy Currents
Main flux generates eddy currents, which generates flux that oppose the main flux.
Eddy current lost is related to i2R, and in reality changes faster than frequency2.
Materials that allows high flux density also has high core loss.

## Slide 26: Example Core Loss Data Plot

## Slide 27: Low Frequency Copper Loss
At low frequency, the copper winding loss is just due to resistance.
Aw is the wire cross-sectional area
ℓb is the length of the wire
The resistivity p increases with higher temperature

## Slide 28: Skin Effect
As frequency increase, there is less and less current at the center and more and more at the edge
The current induce flux, which induces eddy currents in the conductor
The eddy currents cancel out at the middle of the conductor
This increases the resistance of the wire by decreasing its effective cross-sectional area

## Slide 29: Proximity Effect
Conductor 1 and 2 are foils
If #1 has a high frequency current i, and #2 is open, #1 will create a flux that induce a –i and a +i current in #2.
DC component of current doesn’t contribute to proximity loss

## Slide 30: Proximity Effect Example
Each layer carries current i
Layer 1’s power loss is P
Layer 2’s power loss is P due to –i, plus 4P due to +2i, for a total loss of 5P
Layer 3’s loss is 13P

## Slide 31: Leakage Flux in Windings
Most of the leak MMF will be across the open air
Where ℓw = height of the window
Red area enclose 4i
Orange area enclose 8i
Green area enclose 4i

## Slide 32: Interleaving Windings
Interleaving greatly reduces peak MMF, leakage flux, and proximity losses

## Slide 33: Partially-Interleaved Transformer
Primary side current = 3i; secondary side current = 3i/4
Partial interleaving gives partial benefits
Interleaving is only useful if primary and secondary currents are in phase – not useful for sepic or flyback due to currents being out of phase

## Slide 34: Magnetic Device Constraints
Maximum flux density must not saturate the core
Peak ac flux density should be sufficiently small to keep core losses low
Wire size should be small enough to fit in the core window; yet as large as possible to reduce copper loss
Air gap needed if the device is to store energy

## Slide 35: Filter Inductor
Negligible core loss and proximity loss
DC copper loss dominates
Flux density needs to simply avoid saturation
Air gap is employed
Can use core material with high saturation flux density and high core loss

## Slide 36: Coupled Inductor
This is multiple windings sharing the same core
Same guide line as filter inductor
The magnetic equation for this inductor:

## Slide 37: AC Inductor
Core loss, copper loss, proximity loss, are all significant
Flux density is chosen to reduce core loss
Air gap is employed
A high-frequency material (ferrite) must be employed

## Slide 38: Conventional Transformer
Core loss, copper loss, and proximity loss are usually significant
Flux density is chosen to reduce core loss
No air gap employed
A high-frequency material (ferrite) must be employed

## Slide 39: Flyback Transformer - Circuit
When switch is on, iM = i1, and no current goes into the ideal transformer
When switch is off, iM goes into the ideal transformer

## Slide 40: Flyback Transformer
B-H loop like a regular transformer except that it has a DC component
Air gap is used because it’s an inductor for part of the switching cycle
Ferrite material used for the core to reduce core loss
Interleaving the windings have little impact because the primary and secondary windings are out of phase